## Slide 1
Energy Storage Systems
Dr. Chetan B. Khadse

## Slide 2: Battery Performance Characteristics
BATTERY PARAMETERS:
Battery Capacity
Open circuit& terminal voltages
SOC
SD
DOD
Energy Density
power density
Specific energy
Specific Power

## Slide 3: Battery Capacity
The capacity of a battery system is the measure of the amount of free charge generated by the active material at the negative electrode and consumed by the positive electrode.
This parameter is measured in Coulombs (C)
It is generally expressed in Ampere-hour (Ah)
where 1Ah = 3600C
Ah of a battery system which is sometimes denoted by the letter ‘C’ corresponding to the coulometric capacity, is specified under constant current discharge.
Ideally, the Ah rating for a specific battery would be the same for any discharge current.
Practically, actual capacity is dependent on the magnitude of the discharge current
For example, a 20Ah battery could be rated to deliver 1A for 20 hours but instead would not be able to deliver 20A for a complete 1-hour duration

## Slide 4: Energy stored
The energy stored in a battery depends on its voltage, and the charge stored.
The SI unit is the Joule, but this is an inconveniently small unit
Unit- Whr

## Slide 5: Open circuit& terminal voltages
All electric cells have nominal voltages which gives the approximate voltage when the cell is delivering electrical power.
The cells can be connected in series to give the overall voltage required.
V=Terminal voltage
E= Nominal voltage
R=internal resistance

## Slide 6: Self-discharge rates(SD)
The rate at which battery discharges when unused
Most batteries discharge when left unused, and this is known as self-discharge
This is important as it means some batteries cannot be left for long periods without recharging
The rate varies with battery type, and with other factors such as temperature
higher temperatures greatly increase self-discharge

## Slide 7: SOC & DOD
State of charge (SoC) is the level of charge of an electric battery relative to its capacity
The units of SoC are percentage points (0% = empty; 100% = full)
SoC is normally used when discussing the current state of a battery in use
Depth of discharge (DoD): An alternative form of the same measure
It is the the inverse of SoC (100% = empty; 0% = full).
DoD is most often seen when discussing the lifetime of the battery after repeated use.

## Slide 8: Energy density
The battery energy density is the proportion of energy that can be included in a particular unit (mass or capacity)
Energy density is the amount of electrical energy stored per cubic metre of battery volume.
It normally has units of Wh.m−3

## Slide 9: Power density
Power density is the amount of power per unit volume.
In energy transformers including batteries, fuel cells, motors, etc., and also power supply units or similar, power density refers to a volume.
It is then also called volume power density, which is expressed as W/m3.
In SI base units: kg·m−1s−3
SI unit: W/m3

## Slide 10: Charge and Discharge rates(C rate)
The C-rate is a measure of the rate at which a battery is being charged or discharged
It is defined as the current through the battery divided by the theoretical current draw under which the battery would deliver its nominal rated capacity in one hour
It has the units h−1
C-rate is used as a rating on batteries to indicate the maximum current that a battery can safely deliver on a circuit
Standards for rechargeable batteries generally rate the capacity over a 4-hour, 8 hour or longer discharge time

## Slide 11: Battery Specific Energy (SEbatt)
Specific energy is the amount of electrical energy stored for every kilogram of battery mass. It has units of Wh.kg−1 .
The amount of energy per unit of battery mass is termed as the specific energy of battery
expressed in watt-hour per kilogram (Wh/kg). serves as an approximation of the energy deliverable from a battery
commonly used as a reference quantifier between classes of battery technology
The actual energy that can be extracted from a battery system depends on several factors such as the temperature and discharge rate.
As a general expression, the battery specific energy is
Since the discharge energy varies with the discharge rate of the battery, the specific energy of the battery also varies accordingly.

## Slide 12: Battery Specific Power (SPbatt)
Specific power is the amount of power obtained per kilogram of battery. It is a highly variable and rather anomalous quantity, since the power given out by the battery depends far more upon the load connected to it than the battery itself.
The specific power of a battery system is the parameter that quantifies the magnitude of power obtainable per unit mass
Expressed in watt per kilogram (W/kg)
serves as an approximation of the power level available from a battery system