## Slide 1
Unit 3:- HYBRID AND ELECTRIC DRIVETRAINS

## Slide 2: Syllabus…Unit 3 Focus On….
Lecture | Topics to be covered
L1 | Basics about battery, Energy source used for EV’s & HEV’s, Ragone Plot,
L2 | Battery Performance Characteristics- Battery Capacity, Open circuit terminal voltages, Charage and Discharge rates, SOC, SOD, DOD, Battery Energy Density, power density, Specific energy and Specific Power.
L3 | Types of batteries. Comparison of batteries, Ultra capacitors and Ultra flywheels, fuel cells. On board energy sources.
L4 | Charging schemes for EV’s, charging characteristics, different types of charging, CC, CV, CCCV, MSC, Pulse charging & Trickle charging.
L5 | Conductive and wireless power transfer, Inductive Power Transfer, Battery Management system (BMS) for EV and HEV,
L6 | Vehicle to grid configuration, EV energy systems and configuration
L7 | HEV modes of operations starting the system, acceleration and deceleration of the system, normal driving, regenerative braking, the charging of the battery when the vehicle is in motion or when the vehicle is at rest.

## Slide 3: HEV modes of operations
Starting
Acceleration/Deceleration
Normal driving
Regenerative braking
Battery Charging when the vehicle is in motion/Rest

## Slide 4: Starting, Acceleration/Deceleration,Normal driving
For Series HEV configuration:
For starting the system and during normal driving and acceleration, the full system is active
Mechanical energy is transferred from IC engine to the motor via electrical generator together with the energy stored in the battery to the electrical motor
Whole system is active during this mode of operation
During light load on the transmission system:
Mechanical energy is transferred from the IC engine to the electrical motor, a part of it will be used to charge the battery
IC engine operate at maximum efficiency
During light load, part of energy is transferred to the battery for charging

## Slide 5: Deceleration/Breaking
During deceleration –
Regenerative energy is absorbed by battery during braking operation
Energy is recovered from the wheels and the motor is operated as generator and mechanical energy is transferred to the battery via power converter mode
Power converter has to be a bidirectional AC to DC converter if we are using a AC motor

## Slide 6: Battery charging(standstill)
It is possible to charge the battery when the vehicle is at rest
by transferring the mechanical energy available from the IC engine to the battery, by operating, this motor as generator

## Slide 7: Operation modes of a parallel HEV
IC engine is & electrical motor connected to the transmission
These drivetrains are connected individually to the transmission using different clutch
During startup or acceleration, both these systems will be on and maximum power can be transferrd for both startup and acceleration
During normal driving mode
IC engine based drivetrain is active and mechanical energy is transferred to the transmission
Electrical drivetrain is in off mode.

## Slide 8: Deceleration/braking
During deceleration
Electrical drivetrain is only active and power is recovered from the wheels, and the recovered energy stored in the battery by operating the motor as generator
Battery charging
When the vehicle is moving , Battery charging has to be done via transmission.
Mechanical energy required for the transmission has to come from IC engine based system, and a part of it will be transferred to the battery by operating the motor as generator.
Power flow happens through transmission in this case.

## Slide 9: Operation modes of Complex series parallel HEV subsystems
Advantages of both series and parallel configuration
system is complex
Various kind of mode of operation is possible in these systems.
Engine heavy series parallel
HEV Electrical motor heavy series parallel HEV

## Slide 10: IC engine heavy series parallel HEV
Startup:
Only electrical drivetrain
Acceleration:
Mechanical energy is transferred from the IC engine to the transmission in parallel to the electrical drivetrain based battery driven electrical motor type of propulsion
Generator is non-active in this mode

## Slide 11
Normal driving:
IC engine based drivetrain is active, and the mechanical energy is transferred from the IC engine to the transmission, and the rest of the system is inactive. So the electrical drivetrain and the generator is turned off at that time
Deceleration/braking: Electrical drivetrain is active and the mechanical energy of the wheels is extracted by motor operating as generator and the battery is charged by the energy recovered from the wheels

## Slide 12
Charging battery while driving:
While driving, the IC engine drives the transmission and a part of it can be used to charge the battery by operating the electrical generator
IC engine and the generator are connected by a complex planetary gear which enables connection and disconnection of electrical generator during driving operation
When vehicle is not moving or when it is at rest, it’s possible to charge the battery by operating the generator while the mechanical propulsions are off.

## Slide 13: Electric heavy type of series parallel HEV
Startup /light load conditions: Electric mode
Acceleration:
All three propulsion devices or mechanical devices are used to accelerate the system, so the system uses full torque capability of the system
Mechanical energy is transferred from IC engine to the transmission, and a part of it is transferred via generator to the motor
Third is from the battery to the motor

## Slide 14
Normal driving:
IC engine is used to drive the transmission, a part of that mechanical energy is also transferred from generator to the motor for propulsion
In this mode of operation, the battery is not used
Deceleration/Braking :
Similar to IC engine heavy series parallel HEV
Power is recovered only from the electrical drivetrain.

## Slide 15: Battery charging during motion/Standstill
Battery can be charged when the vehicle is in motion, when the mechanical power is transferred from the IC engine to the transmission
Battery charging at stand still is also similar to the IC engine heavy series parallel HEV and it is done by a charging the battery via electrical generator from mechanical power obtained from IC engine.

## Slide 16
END