## Slide 1: Unit 1 Part –II Machine Instructions & Programs

## Slide 2: Outline
Numbers, Arithmetic Operations, and Characters
Memory Locations and Addresses
Memory Operation
Instructions and Instruction Sequencing
Addressing Modes
Assembly Language
Basic Input / Output Operations
Stacks and Queues
Subroutines
Linked List
Encoding of Machine Instructions

## Slide 3: Computer System
Main Memory System
Input/Output System
Arithmetic and
Logic Unit
Operational Registers
Program Counter
Control Unit
Address Data/Instruction
Central Processing Unit (CPU)
Cache memory
Instruction Sets

## Slide 4: Number Representation
Consider an n-bit vector B  bn 1 Kb1b0, where bi =0 or 1 for
0  i  n 1
The vector B can represent unsigned integer values V in the range 0 to 2n 1, where
We need to represent positive and negative numbers for most applications
Three systems are used for representing such numbers
  Sign-and-magnitude
  1’s-complement
  2’s-complement
0
1
V (B)  b  2
n1
n1 1 0
L b  2  b  2

## Slide 5
0000 0
0001 1
0010 2
(+12)
(-5)
Sign + Magnitude
+ = 0
- = 1
0 0101
1’s complement 
10001101
01110010
2’s complement
10001101 (Given no.)
01110010 (1’s complement)
1 (add 1)
-----------------
0111001 1

## Slide 6: Number Systems
In sign-and-magnitude system
  Negative values are represented by changing the most significant bit from 0 to 1
In 1’s-complement system
  Negative values are obtained by complementing each bit of the corresponding positive number
  The operation of forming the 1’s-complement of a given number is equivalent to subtracting that number from 2 n-1
In 2’s-complement system
  The operation of forming the 2’s-complement of a given number is done by subtracting that number from 2 n
The 2’s-complement of a number is obtained by adding 1 to 1’s-complement of that number

## Slide 7: An Example of Number Representations
b3 b2 b1b0
sign and magnitude
0 | 1 | 1 | 1 | +7 | +7 | +7
0 | 1 | 1 | 0 | +6 | +6 | +6
0 | 1 | 0 | 1 | +5 | +5 | +5
0 | 1 | 0 | 0 | +4 | +4 | +4
0 | 0 | 1 | 1 | +3 | +3 | +3
0 | 0 | 1 | 0 | +2 | +2 | +2
0 | 0 | 0 | 1 | +1 | +1 | +1
0 | 0 | 0 | 0 | +0 | +0 | +0
1 | 0 | 0 | 0 | -0 | -7 | -8
1 | 0 | 0 | 1 | -1 | -6 | -7
1 | 0 | 1 | 0 | -2 | -5 | -6
1 | 0 | 1 | 1 | -3 | -4 | -5
1 | 1 | 0 | 0 | -4 | -3 | -4
1 | 1 | 0 | 1 | -5 | -2 | -3
1 | 1 | 1 | 0 | -6 | -1 | -2
1 | 1 | 1 | 1 | -7 | -0 | -1
1’s-complement
2’s-complement

## Slide 8: 2’s-Complement System
+7+(-3)
+7
13 (1101) steps
+4

## Slide 9: Addition of Numbers in 2’s Complement

## Slide 10: Sign Extension of 2’s Complement
Sign extension
  To represent a signed number in 2’s complement form using a larger number of bits, repeat the sign bit as many times as
needed to the left

## Slide 11: Memory Locations
A memory consists of cells, each of which can store a bit of binary information (0 or 1)
Because a single bit represents a very small amount of information
  Bits are seldom handled individually
The memory usually is orga nized so that a group of n bits can be stored or retrieved in a single, basic operation
  Each group of n bits is referred to as a word of information, and n
is called the word length
  A unit of 8 bits is called a byte
Modern computers have word lengths that typically range from 16 to 64 bits

## Slide 12: Memory Addresses
Accessing the memory to store or retrieve a single item of information, either a word or a byte, requires distinct
names or addresses for each item location
It is customary to use numbers from 0 to 2 k-1 as the address space of successive locations in the memory
  K denotes address
  2k-1 denotes address space of memory locations
For example, a 24-bit address generates an address space of 224 (16,777,216) locations
Terminology
  210: 1K (kilo)
  220: 1M (mega)
  230: 1G (giga)
  240: 1T (tera)

## Slide 13
SY
A 2102201 -75
B 2202201 -75
C 2302201-75
A  8 bit  0000 1010

## Slide 14: Memory Words
Word 0
Word 1
Word w-1
n bits
Memory words A signed integer
b31 | b30 |  | b1 | b0
32 bits
8 bits | 8 bits | 8 bits | 8 bits
ASCII
character
Four characters

## Slide 15: Big-Endian & Little-Endian Assignments
Big-endian assignment
Byte address
0 | 1 | 2 | 3
4 | 5 | 6 | 7
2k-4 | 2k-3 | 2k-2 | 2k-1
2k-4
0
4
Word
address
Byte address
3 | 2 | 1 | 0
7 | 6 | 5 | 4
2k-1 | 2k-2 | 2k-3 | 2k-4
2k-4
0
4
Word
address
Little-endian assignment
Byte addresses can be assigned across words in two ways
  Big-endian and little-endian

## Slide 16: Memory Operation
Random access memories must have two basic operations
  Write: writes a data into the specified location
  Read: reads the data stored in the specified location
In machine language program, the two basic operations usually are called
  Store: write operation
  Load: read operation
The Load operation transfers a copy of the contents of a specific memory location to the processor. The memory contents remain unchanged
The Store operation transfers an item of information from the processor to a specific memory location, destroying
the former contents of that location

## Slide 17: Instructions
A computer must have instruct ions capable of performing four types of operations
  Data transfers between the memory and the processor registers
  Arithmetic and logic operations on data
  Program sequencing and control
  I / O transfers
Register transfer notation
  The contents of a location are denoted by placing square brackets around the name of the location
  For example, R1 €[LOC] means that the contents of memory location LOC are transferred into processor register R1
  As another example, R3€[R1]+[R2] means that adds the contents of registers R1 and R2, and then places their sum into register R3

## Slide 18: C = A + B
Read A
Read B
Add A, B
Move B, C
Print C
OPCODE | Operand list |  | 
ADD | A Source operand | B Destination operand | 

## Slide 19: Assembly Language Notation
Types of instructions
  Zero-address instruction
  One-address instruction
  Two-address instruction
  Three-address instruction
Zero-address instruction
  For example, store operands in a structure called a pushdown stack
One-address instruction
  Instruction form: Operation Destination
  For example, Add A: add the contents of memory location A to the contents of the accumulator register and place the sum back into the accumulator
  As another example, Load A: copies the contents of memory location A into the accumulator

## Slide 20: Assembly Language Notation
Two-address instruction
  Instruction form: Operation Source, Destination
  For example, Add A, B: performs the operation B€[A]+[B].
When the sum is calculated, the result is sent to the memory and stored in location B
  As another example, Move B, C : performs the operation C€[B], leaving the contents of location B unchanged
Three-address instruction
  Instruction form: Operation Source1, Source2, Destination
  For example, Add A, B, C: adds A and B, and the result is sent to the memory and stored in location C
  If k bits are needed to specify the memory address of each
operand, the encoded form of the above instruction must contain 3k bits for addressing purposes in addition to the bits needed to denote the Add operation

## Slide 21: Instruction Execution
How a program is executed
  The processor contains a register called the program counter (PC), which holds the address of the instruction to be executed next. To begin executing a program, the address of its first instruction
must be placed into the PC, then the processor control circuits use the information in the PC to fetch and execute instruction, one at a time, in the order of increasing address
Basic instruction cycle
START
Fetch Instruction
Execute Instruction
HALT

## Slide 22: A Program for C=[A]+[B]
Move A, R0 Add B, R0
Move R0, C
3-instruction program
segment
Data for
the program
Address
i i+4 i+8
A
B
C
R0

## Slide 23: Straight-Line Sequencing
Move NUM1, R0
Add NUM2, R0
Add NUM3, R0
Add NUMn, R0
Move R0, SUM
i i+4 i+8
i+4n-4 i+4n
SUM NUM1 NUM2
NUMn

## Slide 24: Branching
SUM N
NUM1
Move N, R1
Clear R0
Determine address of
“Next” number to R0
Decrement R1
Branch>0 LOOP
Move R0, SUM
n
LOOP
“Next” number and add
Program
loop
NUMn

## Slide 25: Condition Codes
The processor keeps track of information about the results of various operations for use by subsequent conditional
branch instructions. This is accomplished by recoding
required information in individual bits, often called
condition code flags
Four commonly used flags are
  N (negative): set to 1 if the results is negative; otherwise, cleared to 0
  Z (zero): set to 1 if the result is 0; otherwise, cleared to 0
  V (overflow): set to 1 if arithmetic overflow occurs; otherwise, cleared to 0
  C (carry): set to 1 if a carry-out results from the operation; otherwise, cleared to 0
N and Z flags caused by an arithmetic or a logic operation, V and C flags caused by an arithmetic operation

## Slide 26: Addressing Modes
Programmers use data structures to represent the data used in computations. These include lists, linked lists, array, queues, and so on
A high-level language enables the programmer to use
constants, local and global variables, pointers, and arrays
When translating a high-level language program into assembly language, the compiler must be able to
implement these constructs using the facilities in the instruction set of the computer
The different ways in which the location of an operand is specified in an instruction are referred to as addressing modes

## Slide 27: Generic Addressing Modes
Name |  | Assembler syntax | Addressing function
Immediate |  | #Value | Operand=Value
Register |  | Ri | EA=Ri
Absolute (Direct) |  | LOC | EA=LOC
Indirect |  | (Ri) | EA=[Ri]
 |  | (LOC) | EA=[LOC]
Index |  | X(Ri) | EA=[Ri]+X
Base with index |  | (Ri, Rj) | EA=[Ri]+[Rj]
Base with index and | offset | X(Ri, Rj) | EA=[Ri]+[Rj]+X
Relative |  | X(PC) | EA=[PC]+X
Autoincrement |  | (Ri)+ | EA=[Ri]; Increment Ri
Autodecrement |  | -(Ri) | Decrement Ri; EA=[Ri]
EA: effective address Value: a signed number

## Slide 28: Register, Absolute and Immediate Modes
Register mode: the operand is the contents of a processor register; the name (address) of the register is given in the instruction
  For example, Add Ri, Rj (adds the contents of Ri and Rj and the result is stored in Rj)
Absolute mode: the operand is in a memory location; the address of this location is given explicitly in the
instruction. (In some assembly languages, this mode is
called Direct)
  For example, Move LOC, R2 (moves the content of the memory with address LOC to the register R2)
  The Absolute mode can represent global variables in a program. For example, a declaration such as Integer A, B;
Immediate mode: the operand is given explicitly in the instruction

## Slide 29: Indirection and Pointers
Indirect mode: the effective address of the operand is the contents of a register or memory location whose address appears in the instruction
Indirection is denoted by placing the name of the register or the memory address given in the instruction in
parentheses
The register or memory locati on that contains the address of an operand is called a pointer

## Slide 30: Two Types of Indirect Addressing
Add (R1), R0
Operand
Main Memory
B
B
R1
Register
Through a general-purpose register
Through a memory location
Add (A), R0
B
Operand
A
B

## Slide 31: Register Indirect Addressing Diagram
 | Opcode | Register Address R | 
Instruction
Operand
Memory
Pointer to Operand
Registers

## Slide 32: Using Indirect Addressing in a Program
Address | Contents | 
 | Move Move Clear | N, R1 #NUM1, R2 R0
LOOP | Add Add Decrement Branch>0 | (R2), R0 #4, R2 R1 LOOP
 | Move | R0, SUM
Initialization

## Slide 33: Indexing and Arrays
Index mode: the effective address of the operand is
generated by adding a constant value to the contents of a register
  The register used may be either a special register provided for this purpose, or, more commonly, it ma y be any one of a set of general- purpose registers in the processor. It is referred to as an index register
  The index mode is useful in dealing with lists and arrays
  We denote the Index mode symbolically as X(Ri), where X denotes the constant value contained in the instruction and Ri is the name of the register involved. The effective address of the operand is given by EA=X+(Ri). The contents of the index register are not
changed in the process of generating the effective address

## Slide 34: Indexed Addressing
Add 20(R1), R2
Operand
1000
Offset=20
1020
1000
R1
Offset is given as a constant

## Slide 35: Indexed Addressing
Add 1000(R1), R2
Operand
1000
Offset=20
1020
20
R1
Offset is in the index register

## Slide 36: An Example for Indexed Addressing
N LIST
LIST+4 LIST+8 LIST+12
LIST+16
n
Student ID
Test 1
Test 2
Test 3
Student ID
Test 1
Test 2
Test 3
 | Move | #LIST, R0
 | Clear | R1
 | Clear | R2
 | Clear | R3
 | Move | N, R4
 | LOOP Add | 4(R0), R1
 | Add | 8(R0), R2
 | Add | 12(R0), R3
 | Add | #16, R0
 | Decrement | R4
 | Branch>0 | LOOP
 | Move | R1, SUM1
 | Move | R2, SUM2
 | Move | R3, SUM3

## Slide 37: Variations of Indexed Addressing Mode
A second register may be used to contain the offset X, in which case we can write the Index mode as (Ri,Rj)
  The effective address is the sum of the contents of registers Ri and Rj
  The second register is usually called the base register
  This mode implements a two-dimensional array
Another version of the Index mode use two registers plus a constant, which can be denoted as X(Ri,Rj)
  The effective address is the sum of the constant X and the contents of registers Ri and Rj
  This mode implements a three-dimensional array

## Slide 38: Additional Modes
Autoincrement mode: the effective address of the operand is the contents of a register specified in the instruction.
After accessing the operand, the contents of this register
are automatically incremented to point to the next item in a list
  The Autoincrement mode is denoted as (Ri)+
Autodecrement mode: the contents of a register specified in the instruction are first automatically decremented and are then used as the effective address of the operand
  The Autodecrement mode is denoted as –(Ri)

## Slide 39: An Example of Autoincrement Addressing
LOOP
Move Move Clear Add
Decrement Branch>0 Move
N, R1
#NUM1, R2 R0
(R2)+, R0 R1
LOOP R0, SUM

## Slide 40: Assembly Language
A complete set of symbolic names and rules for their use constitute a programming language, generally referred to as an assembly language
Programs written in an assembly language can be
automatically translated into a sequence of machine instructions by a program called an assembler
When the assembler program is executed, it reads the user program, analyzes it, and then generates the desired
machine language program
The user program in its origin al alphanumeric text format is called a source program, and the assembled machine
language program is called an object program

## Slide 41: Assembler Directives
In addition to providing a mechanism for representing instructions in a program, the assembly language allows the programmer to specify ot her information needed to translate the source program into the object program
Suppose that the name SUM is used to represent the value
200. The fact may be conveyed to the assembler program through a statement such as
  SUM EQU 200
This statement does not denote an instruction that will be executed when the object program is run; it will not even appear in the object program
  Such statements, called assembler directives (or commands)

## Slide 42: Assembler
Assembler directives | SUM | EQU | 200
 |  | ORIGIN | 204
 | N | DATAWORD | 100
 | NUM1 | RESERVE | 400
 |  | ORIGIN | 100
Statements that | START | MOVE | N, R1
generate MOVE #NUM1, R2 |  |  | 
machine |  | CLR | R0
instructions | LOOP | ADD | (R2), R0
 |  | ADD | #4, R2
 |  | DEC | R1
 |  | BGTZ | LOOP
 |  | MOVE | R0, SUM
Assembler directives |  | RETURN | 
 |  | END | START
100
104
108
112
116
120
124
128
132
Move N, R1
Move #NUM1, R2
Clear R0
Add (R2) , R0
Add #4, R2
Decrement R1
Branch>0 LOOP
Move R0, SUM
100
UM 200
N 204
Memory arrangement
Assembly language representation

## Slide 43: Number Notation
When dealing with numerical values, most assemblers allow numerical values to be specified in different ways
For example, consider the number 93, which is represented by the 8-bit binary number 01011101. If the value is to be
used as immediate operand,
  It can be given as a decimal number , as in the instruction ADD #93, R1
  It can be given as a binary number, as in the instruction ADD #%01011101,R1 (a binary number is identified by a prefix symbol such as percent sign)
  It also can be given as a hexadecimal number, as in the instruction ADD #$5D, R1 (a hexadecimal num ber is identified by a prefix
symbol such as dollar sign)

## Slide 44: Basic Input/Output Operations
Bus connection for processor, keyboard, and display
Processor
DATAIN
Display
SIN
Keyboard
DATAOUT
SOUT
010
10
DATAIN, DATAOUT: buffer registers SIN, SOUT: status control flags

## Slide 45: Wait Loop
In order to perform I / O transfers, we need machine
instructions that can check the state of the status flags and transfer data between the processor and I / O device
Wait loop for Read operation
READWAIT
Branch to READWAIT if SIN=0 Input from DATAIN to R1
Wait loop for Write operation
  WRITEWAIT Branch to WRITEWAIT if SOUT=0 Output from R1 to DATAOUT
We assume that the initial stat e of SIN is 0 and the initial state of SOUT is 1

## Slide 46: Memory-Mapped I/O
Many computers use an arrangement called memory-
mapped I / O in which some memory address values are
used to refer to peripheral device buffer registers, such as DATAIN and DATAOUT
Thus no special instructions are needed to access the
contents of these registers; data can be transferred between these registers and the processor using instructions that we have discussed, such as Move, Load, or Store
Also, the status flags SIN and SOUT can be handled by including them in device status registers, one for each of the two devices

## Slide 47: Read and Write Programs
Assume that bit b 3 in registers INSTATUS and
OUTSTATUS corresponds to SIN and SOUT, respectively
Read Loop
READWAIT
Testbit Branch=0 MoveByte
#3, INSTATUS READWAIT
DATAIN, R1
Write Loop
  WRITEWAIT
Testbit #3, OUTSTATUS
Branch=0 WRITEWAIT
MoveByte R1, DATAOUT

## Slide 48: Stacks and Queues
A stack is a list of data elem ents, usually words or bytes, with the accessing restriction that elements can be added or removed at one end of the list only
  It is also called a last-in-first-out (LIFO) stack
  A stack has two basic operations: push and pop
  The terms push and pop are used to describe placing a new item on the stack and removing the top item from the stack,
respectively.
Another useful data structure that is similar to the stack is called a queue
  Data are stored in and retrieved from a queue on a first-in-first- out (FIFO) basis
  Two pointers are needed to keep track of the two ends of the queue

## Slide 49: A Stack of Words in the Memory
SP
Stack pointer register
-28
17
739
43
Stack
BOTTOM
Current top element
Bottom element
Low address
High address

## Slide 50: Push and Pop Operations
Assume that a byte-addressable memory with 32-bit words
The push operation can be implemented as
Subtract Move
#4, SP NEWITEM, (SP)
The pop operation can be implemented as
Move (SP), ITEM Add #4, SP
If the processor has the Autoincrement and Autodecrement addressing modes, then the push operation can be
implemented by the single instruction
Move NEWITEM, -(SP)
And the pop operation can be implemented as
Move (SP)+, ITEM

## Slide 51: Examples
19
-28
17
43
19
SP SP
NEWITEM
-28
17
43
-28
SP SP
ITEM
Push operation
Pop operation

## Slide 52: Checking for Empty and Full Errors
When a stack is used in a program, it is usually allocated a fixed amount of space in the memory
  We must avoid pushing an item onto the stack when the stack has reached in its maximum si ze, i.e., the stack is full
  On the other hand, we must avoid popping an item off the stack when the stack has reached in its minimum size, i.e., the stack is empty
Routine for a safe pop or a safe push operation
  Compare src, dst
  Perform [dst]-[src]
  Sets the condition code flags according to the result

## Slide 53: Subroutines
In a given program, it is often necessary to perform a particular subtask many times on different data valu es. Such a subtask is called a subroutine.
The location where the calling program resumes execution is the location pointed by the updated PC while the Call
instruction is being executed. Hence the contents of the PC must be saved by the Call instru ction to enable correct return to the calling program
Memory location
Calling program
Memory location
Subroutine SUB
.
.
.
Call SUB
next instruction
200
204
.
.
.
1000
first instruction
.
.
.
Return

## Slide 54: Subroutine Linkage
The way in which a computer makes it possible to call and return from subroutines is referred to as its
subroutine linkage method
Subroutine linkage using a link register
1000
204
PC
Link
204
Call
Return

## Slide 55: Subroutine Nesting
A common programming practice, called subroutine nesting, is to have one subroutine call another
Subroutine nesting call be carried out to any depth.
Eventually, the last subroutine called completes its
computations and returns to the subroutine that called it
The return address needed for this first returns is the last one generated in the nested call sequence. That is, return addresses are generated and used in a last-in-first-out
order
Many processors do this by using a stack pointer and the stack pointer points to a stack called the processor stack

## Slide 56: Example of Subroutine Nesting
C+4
BA++44
AA++44
Main Program SUB 1 SUB 2
SUB 3
A
. . .
.
.
.
.
.
.
.
.
.
B
C

## Slide 57: Example of Subroutine Nesting
jr $ra
abc
Save
Restore
PC
jal abc | Prepare to call
 | Prepare to continue
main
jal xyz
jr $ra
xyz
Procedure
abc
Procedure
xyz
[Source: B. Parhami, UCSB]

## Slide 58: Parameter Passing
When calling a subroutine, a program must provide to the subroutine the parameters, that is, the operands or
their addresses, to be used in the computation. Later, the subroutine returns other parameters, in this case, the
result of computation
The exchange of information between a calling program and a subroutine is referre d to as parameter passing
Parameter passing approaches
  The parameters may be placed in registers or in memory locations, where they can be accessed by the subroutine
  The parameters may be placed on the processor stack used for saving the return address

## Slide 59: Passing Parameters with Registers
N, R1
#NUM1, R2
Calling program
Move Move Call
LISTADD R0, SUM
R1 serves as a counter R2 points to the list Call subroutine
Save result
M.ove
Subroutine
LISTADD LOOP
.
.
Clear Add
R0
(R2)+, R0
Initialize sum to 0 Add entry from list
Decrement R1
Branch>0 LOOP Return
Return to calling program
passed by value
passing by reference

## Slide 60: Passing Parameters with Stack
Assume top of stack is at level 1 below.
(top of stack at level 1)
.
.
.
R0-R2, -(SP)
Move | #NUM1, -(SP) | Push parameters onto stack
Move | N, -(SP) | 
Call | LISTADD | Call subroutine
 |  | (top of stack at level 2)
Move | 4(SP), SUM | Save result
Add | #8, SP | Restore top of stack Level
LISTADD MoveMultiple
Save registers
(top of stack at level 3) Initialize counter to N.
Move Move Clear Add
Decrement Branch>0 Move MoveMultiple Return
16(SP), R1
20(SP), R2 R0
(R2)+, R0 R1
LOOP
R0, 20(SP)
(SP)+, R0-R2
Initialize pointer to the list
Initialize sum to 0 Add entry from list
Put result on the stack Restore registers
Return to calling program
LOOP
[R2]
[R1]
[R0]
Return address
N
NUM1
3
Level 2
Level 1

## Slide 61: Stack Frame
Saved [R1]
Saved [R0]
localvar3
localvar2
localvar1
saved [FP]
Return address
param1
param2
param3
param4
SP (Stack pointer)
-12(FP)
-8(FP)
-4(FP)
FP (Frame pointer)
Stack frame
8(FP)
12(FP)
16(FP)
20(FP)

## Slide 62: Shift Instructions
Logical shifts
Logic shift left
LShiftL #2, R0
Arithmetic shifts
shift right
AShiftR #2, R0
1 | 1 | 0 | . | . | . | . | . | . | 0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0 | . | . | . | . | . | . | 0 | 1 | 1
0
1
Before:
After:
R0
0
C
Carry flag
1 | 0 | 0 | 1 | 1 | . | . | . | . | . | . | 0 | 1 | 0
1 1 1 0 0 1 1 . . . . . . . 0
0
1
Before:
After:
R0
C
Sign bit

## Slide 63: Rotate Instructions
Rotate left without carry
RotateL #2, R0
After: | 1 | 1 | 1 | 0 | . . . . . . | 0 | 1 | 1 | 0 | 0
 | C |  |  |  |  |  |  | R0 |  |  | 
Before: | 0 |  |  | 0 | 1 | 1 | 1 | 0 . . . . . . | 0 | 1 | 1
After: | 1 |  |  | 1 | 1 | 0 | . . | . . . . 0 1 | 1 | 0 | 1
Rotate left with carry RotateLC #2, R0 |  |  |  |  |  |  |  |  |  |  | 
 | C |  |  |  |  |  |  | R0 |  |  | 
Before: | 0 |  |  | 0 | 1 | 1 | 1 | 0 . . . . . . | 0 | 1 | 1

## Slide 64: Linked List
Record 1
Record 2
Record k
0
Link address
Head
Tail
Record 1
Record 2
New Record
Linking structure
Inserting a new record

## Slide 65: A List of Student Test Scores
27243 | 1040 |  |  | 
28106 | 1200 |  |  | 
1040
28370 | 2880 |  |  | 
1200
40632 | 1280 |  |  | 
2720
47871 | 0 |  |  | 
1280
Address Key field Link field
2320
Data field
Head
Tail
First record
Second record
Last

## Slide 66: Encoding of Machine Instructions
To be executed in a processor, an instruction must be encoded in a compact binary pattern. Su ch encoded instructions are
properly referred to as machine instructions. The instructions
that use symbolic names and acronyms are called assembly language instructions, which are converted into the machine instructions using assembler program
For a given instruction, the type of operation that is to be
performed and the type of oper ands used may be specified using an encoded binary pattern referred to as the OP code
In addition to the OP code, th e instruction has to specify the source and destination registers, and addressing mode, etc,

## Slide 67: Examples
Assume that 8 bits are allocate d for OP code, and 4 bits are needed to identify each register, and 6 bits are needed to
specify an addressing mode
The instruction Move 24(R0), R5
  Require 16 bits to denote the OP code and the two registers
  Require 6 bits to choose the addressing mode
  Only 10 bits are left to give the index value
The instruction LshiftR #2, R0
  Require 18 bits to specify the OP code, the addressing modes, and the register
  This limits the size of the immediate operand to what is expressible in 14 bits
In the two examples, the instructions can be encoded in a 32-bit word.

## Slide 68: Encoding Instructions into 32-bit Words
OP code | Source | Destination | Other info
8
7
7
10
OP code | Source | Destination | Other info
Memory address / Immediate operand |  |  | 
One-word instruction
Two-word instruction
OP code | Ri | Rj | Rk | Other info
Three-operand instruction

## Slide 69: Encoding Instructions into 32-bit Words
But, what happens if we want to specify a memory operand using the Absolute addressing mode?
The instruction Move R2, LOC
  Require 18 bits to denote the OP code, the addressing modes, and the register
  The leaves 14 bits to express the address that corresponds to LOC, which is clearly insufficient
If we want to be able to give a complete 32-bit address in the instruction, an instruction must have two words
If we want to handle this type of instructions: Move LOC1, LOC2
  An instruction must have three words

## Slide 70: CISC & RISC
Using multiple words, we can implement quite complex instructions, closely resembling operations in high-level programming language
The term complex instruction set computer (CISC) has been used to refer to processors that use instruction sets of this type
The restriction that an instru ction must occupy only one word has led to a style of computers that have become
known as reduced instruction set computer (RISC)