## Slide 1: Unit 2 Input/Output Ports & Memory Systems

## Slide 2: Outline
Accessing I / O Devices
Interrupts
Direct Memory Access
Buses
Interface Circuits
Standard I / O Interfaces

## Slide 3: Content Coverage
Main Memory System
Input/Output System
Operational
Registers Arithmetic and
Program Logic Unit
Counter
Control Unit
Address Data/Instruction
Central Processing Unit (CPU)
Cache
memory
Instruction Sets

## Slide 4: Accessing I/O Devices
Single-bus structure
  The bus enables all the devices connected to it to exchange information
  Typically, the bus consists of three sets of lines used to carry address, data, and control signals
  Each I / O device is assigned a unique set of addresses
Processor
Memory
I/O device 1
I/O device n
Bus

## Slide 5: I/O Mapping
Memory mapped I / O
  Devices and memory share an address space
  I / O looks just like memory read / write
  No special commands for I/ O
    Large selection of memory access commands available
Isolated I / O
  Separate address spaces
  Need I / O or memory select lines
  Special commands for I /O
    Limited set

## Slide 6: Memory-Mapped I/O
When I / O devices and the memory share the same address space, the arrangement is called memory- mapped I / O
With memory-mapped I / O, any machine instruction that can access memory can be used to transfer data to or from an I / O device
Most computer systems use memory-mapped I / O.
Some processors have special IN and OUT instructions to perform I / O transfers
  When building a computer system based on these processors, the designer has the option of connecting I / O devices to usethe special I / O address space or simply incorporating them as part of the memory address space

## Slide 7: I/O Interface for an Input Device
The address decoder, the data and status registers, and the control circuitry required to coordinate
I / O transfers constitute the device’s interface circuit
Control
circuits
Address decoder
Data and status
registers
Bus
Address lines Data lines Control lines
Input device

## Slide 8: I/O Techniques
Programmed
Interrupt driven
Direct Memory Access (DMA)

## Slide 9: Program-Controlled I/O
Consider a simple example of I / O operations involving a keyboard and a display device in a computer system. The four registers shown below are used in the data transfer operations
  The two flags KIRQ and DIRQ in STATUS register are
used in conjunction with interrupts
DATAIN
DATAOUT
STATUS CONTROL
 |  |  |  | DIRQ | KIRQ | SOUT | SIN
 |  |  |  | DEN | KEN |  | 
7
6
5
4
3
2
1
0

## Slide 10: An Example
 | Move | #LINE, R0 | Initialize memory pointer
WAITK | TestBit | #0,STATUS | Test SIN
 | Branch=0 | WAITK | Wait for character to be entered
 | Move | DATAIN,R1 | Read character
WAITD | TestBit | #1,STATUS | Test SOUT
 | Branch=0 | WAITD | Wait for display to become ready
 | Move | R1,DATAOUT | Send character to display
 | Move | R1,(R0)+ | Store character and advance pointer
 | Compare | #$0D,R1 | Check if Carriage Return
 | Branch=0 | WAITK | If not, get another character
 | Move | #$0A,DATAOUT | Otherwise, send Line Feed
 | Call | PROCESS | Call a subroutine to process the
 |  |  | input line
A program that reads one line from the keyboard, stores it in memory buffer, and echoes it back to the display

## Slide 11: Program-Controlled I/O
The example described above illustrates program- controlled I / O, in which the processor repeatedly checks a status flag to achieve the required synchronization between the processor and an input or output device. We say that the processor polls the devices
There are two other commonly used mechanisms for implementing I / O operations: interrupts and direct memory access
  Interrupts: synchronization is achieved by having the I / O device send a special signal over the bus whenever it is ready for a data transfer operation
  Direct memory access: it involves having the device interface transfer data directly to or from the memory

## Slide 12: Interrupts
To avoid the processor being not performing any useful computation, a hardware signal called an interrupt to the processor can do it. At least one of the bus control lines, called an interrupt-request line, is usually dedicated for this purpose
An interrupt-service routine usually is needed and is executed when an interrupt request is issued
On the other hand, the processor must inform the device that its request has been recognized so that it may remove its interrupt-request signal. An interrupt-acknowledge signal serves this function

## Slide 13: Example
Program 1 COMPUTE routine
Program 2 PRINT routine
Interrupt occurs here
1
2
i i+1
M

## Slide 14: Interrupt-Service Routine & Subroutine
Treatment of an interrupt-service routine is very similar to that of a subroutine
An important departure from the similarity should be noted
  A subroutine performs a function required by the program from which it is called.
  The interrupt-service routine may not have anything in common with the program being executed at the time the interrupt request is received. In fact, the two programs often belong to different users
Before executing the interrupt-service routine, any information that may be altered during the execution of that routine must be saved. This information must be restored before the interrupted program is resumed

## Slide 15: Interrupt Latency
The information that needs to be saved and restored typically includes the condition code flags and the contents of any registers used by both the interrupted program and the interrupt-service routine
Saving registers also increases the delay between the time an interrupt request is received and the start of execution of the interrupt-service routine. The delay is called interrupt latency
Typically, the processor saves only the contents of
the program counter and the processor status register. Any additional information that needs to be saved must be saved by program instruction at the beginning of the interrupt-service routine and restored at the end of the routine

## Slide 16: Interrupt Hardware
INTR
INTR1
INTR2
INTRn
INTR
An equivalent circuit for an open-drain bus used to implement a common interrupt-request line
Vdd
Processor
R
INTR=INTR1+INTR2+…+INTRn

## Slide 17: Handling Multiple Devices
Handling multiple devices gives rise to a number of questions:
  How can the processor recogniz e the device requesting an
interrupt?
  Given that different devices are likely to require different interrupt-service routines, how can the processor obtain the starting address of the approp riate routine in each case?
  Should a device be allowed to interrupt the processor while another interrupt is being serviced?
  How should two or more simult aneous interrupt request be handled?
The information needed to determine whether a device is requesting an interrupt is available in its status register
  When a device raises an interrupt request, it sets to 1 one of
the bits in its status register , which we will call the IRQ bit

## Slide 18: Identify the Interrupting Device
The simplest way to identify the interrupting device is to have the interrupt-service routine poll all the
I / O devices connected to the bus
The polling scheme is easy to implement. Its main disadvantage is the time spen t interrogating all the devices
A device requesting an interrupt may identify itself directly to the processor. Then, the processor can immediately start executing the corresponding interrupt-service routine. This is called vectored interrupts
An interrupt request from a high-priority device should be accepted while the processor is servicing another request from a lower-priority device

## Slide 19: Interrupt Priority
The processor’s priority is usually encoded in a few bits of the processor status word. It can be changed by program instructions that write into the program status register (PS). These are privileged instructions, which can be executed only while the processor is running in the supervisor mode
The processor is in the su pervisor mode only when executing operating system routines. It switches to the user mode before beginning to execute application program
An attempt to execute a privileged instruction while in the user mode leads to a special type of interrupt called a privilege exception

## Slide 20: Implementation of Interrupt Priority
An example of the implementation of a multiple- priority scheme
Processor
Device 1
Device 2
Device p
INTA1
INTR1
Priority arbitration circuit
INTRp
INTAp

## Slide 21: Simultaneous Requests
Consider the problem of simultaneous arrivals of interrupt requests from two or more devices. The processor must have some means of deciding which request to service first
Interrupt priority scheme with daisy chain
Device 1
Device 2
Device n
INTA
INTR
Processor

## Slide 22: Priority Group
Combination of the interrupt priority scheme with daisy chain and with individual interrupt- request and interrupt-acknowledge lines
Processor
Priority arbitration circuit
Device
Device
Device
INTA1
INTR1
Device
Device
Device
INTAp
INTRp

## Slide 23: Direct Memory Access
To transfer large blocks of data at high speed, a special control unit may be provided between an external device and the main memory, without continuous intervention by the processor. This approach is called direct memory access (DMA)
DMA transfers are performed by a control circuit that is part of the I / O device in terface. We refer to this circuit as a DMA controller.
Since it has to transfer blocks of data, the DMA controller must increment the memory address for successive words and keep track of the number of transfers

## Slide 24: DMA Controller
Although a DMA controller can transfer data without intervention by the processor, its operation must be under the control of a program executed by the processor
An example
31 30 1 0
Status and control
IRQ
IE
Starting address
Word count
Done
R/W

## Slide 25: DMA Controller in a Computer System
Processor
Main memory
Disk/DMA
controller
System bus
DMA
controller
Printer
Keyboard
Disk
Disk
Network
Interface

## Slide 26: Memory Access Priority
Memory accesses by the processor and the DMA controllers are interwoven. Request by DMA devices for using the bus are always given higher priority than processor requests.
Among different DMA devices, top priority is given to high-speed peripherals such as a disk, a high- speed network interface, etc.
Since the processor originates most memory access cycles, the DMA controller can be said to “steal” memory cycles from the processor. Hence, this interweaving technique is usually called cycle stealing
The DMA controller may transfer a block of data without interruption. This is called block/burst mode

## Slide 27: Bus Arbitration
A conflict may arise if both the processor and a DMA controller or two DMA controllers try to use the bus at the same time to access the main memory. To resolve this problem, an arbitration procedure on bus is needed
The device that is allowed to initiate data transfer on the bus at any given time is called the bus master. When the current master relinquishes control of the bus, another device can acquire this status
Bus arbitration is the process by which the next device to become the bus master take into account the needs of various devices by establishing a priority system for gaining access to the bus

## Slide 28: Bus Arbitration
There are two approaches to bus arbitration
  Centralized and distributed
In centralized arbitration, a single bus arbiter performs the required arbitration
In distributed arbitration, all devices participate in the selection of the next bus master

## Slide 29: Centralized Arbitration
DMA
Controller 1
BG1
Processor
DMA
Controller 2
BBSY
BR
BG2
BR
BG1 BG2
BBSY
Processor
DMA controller 2
Processor

## Slide 30: Buses
A bus protocol is the set of rules that govern the behavior of various devices connected to the bus as to when to place information on the bus, assert control signals, and so on
In a synchronous bus, all devices derive timing information from a common clock line. Equal spaced pulses on this line define equal time intervals
In the simplest form of a synchronous bus, each of these intervals constitutes a bus cycle during which one data transfer can take place

## Slide 31: Interface Circuits
Keyboard to processor connection
  When a key is pressed, the Valid signal changes from 0 o 1, causing the ASCII code to be loaded into DATAIN and SIN to be set to 1
  The status flag SIN is cleared to 0 when the processor
reads the contents of the DATAIN register
Processor
Encoder and Debouncing circuit
DATAIN
SIN
Input Interface
Keyboard switches
Valid
Data
Data
Address
Master-ready
Slave-ready
R/W

## Slide 32: Printer to Processor Connection
The interface contains a data register, DATAOUT, and a status flag, SOUT
  The SOUT flag is set to 1 when the printer is ready to accept another character, and it is cleared to 0 when a new character is loaded into DATAOUT by the processor
  When the printer is ready to acce pt a character, it asserts its idle signal
Processor
DATAOUT
SOUT
Output
Interface
Data
Address
Master-ready
Slave-ready
R/W
Printer
Idle
Data
Valid

## Slide 33: Serial Port
A serial port is used to connect the processor to
I / O devices that require transmission of data one bit at a time
The key feature of an interface circuit for a serial port is that it is capable of communicating in a bit-serial fashion on the device side and in a bit- parallel fashion on the bus side
The transformation between the parallel and serial formats is achieved with shift registers that have parallel access capability

## Slide 34
Shift Register
8 bit register == 8 bit data
4 modes
Serial In Serial Out (SISO)
Serial In Parallel Out (SIPO)
Parallel In Serial Out (PISO)
Parallel In Parallel Out (PIPO)

## Slide 35: A Serial Interface
Input shift register
DATAIN
DATAOUT
Output shift register
Serial input
Serial output
D7
D0

## Slide 36: Standard I/O Interfaces
The processor bus is the bus defined by the signals on the processor chip itself. Devices that require a very high speed connection to the processor, such as the main memory, may be connected directly to this bus
The motherboard usually provides another bus that can support more devices.
The two buses are interconnected by a circuit, which we called a bridge, that translates the signals and protocols of one bus into those of the other
It is impossible to define a uniform standards for the processor bus. The structure of this bus is closely tied to the architecture of the processor
The expansion bus is not subject to these limitations, and therefore it can use a standardized signaling structure

## Slide 37: Peripheral Component Interconnect Bus
Use of a PCI bus in a computer system
Host
Main memory
Disk
PCI Bus
Printer
Ethernet interface
PCI
bridge

## Slide 38: PCI Bus
The bus support three independent address spaces: memory, I / O, and configuration.
The I / O address space is intended for use with processors, such Pentium, that have a separate I / O address space.
However, the system designer may choose to use memory-mapped I / O even when a separate I / O address space is available
The configuration space is intended to give the PCI its plug-and-play capability.
  A 4-bit command that accompanies the address identifies which of the three spaces is being used in a given data transfer operation

## Slide 39: Universal Serial Bus (USB)
The USB has been designed to meet several key objectives
  Provide a simple, low-cost, and easy to use interconnection system that overcomes the difficulties due to the limited number of I / O ports available on a computer
  Accommodate a wide range of data transfer characteristics for I / O devices, including telephone and Internet connections
  Enhance user convenience through a “plug-and-play” mode of operation

## Slide 40: USB Structure
A serial transmission format has been chosen for the USB because a serial bus satisfies the low-cost and flexibility requirements
Clock and data information are encoded together and
transmitted as a single signal
  Hence, there are no limitations on clock frequency or distance arising from data skew
To accommodate a large number of devices that can be added or removed at any time, the USB has the tree structure
  Each node of the tree has a device called a hub, which acts as an
intermediate control point between the host and the I / O device
  At the root of the tree, a root hub connects the entire tree to the host computer

## Slide 41: USB Tree Structure
Host Computer
Root hub
Hub
Hub
Hub
I/O device
I/O device
I/O device
I/O device
I/O device
I/O device

## Slide 42: USB Tree Structure
The tree structure enables many devices to be connected while using only simple point-to-point serial links
Each hub has a number of ports where devices may be connected, including other hubs
In normal operation, a hub copies a message that it receives from its upstream connection to all its downstream ports
  As a result, a message sent by th e host computer is broadcast to all I / O devices, but only the addresse d device will respond to that message
A message sent from an I / O de vice is sent only upstream towards the root of the tree and is not seen by other devices
  Hence, USB enables the host to communicate with the I / O devices, but it does not enable these devices to communicate with each other

## Slide 43: USB Protocols
All information transferred over the USB is organized in packets, where a packet consists of one or more bytes of information
The information transferred on the USB can be divided into two broad categories: control and data
  Control packets perform such tasks as addressing a device to initiate data transfer, acknowledging that data have been received correctly, or indicating an error
  Data packets carry informatio n that is delivered to a device. For example, input and output data are transferred inside data packets