## Slide 1: Unit 4:Finite State Machines
Mealy and
Moore machines representation
Basic design steps
Finite state machine design, Sequence
detector moore and mealy, Serial
binary adder

## Slide 2: Finite State Machine
A synchronous sequential circuit is also called as Finite State Machine FSM, if it has finite number of states. There are two types of FSMs.
Mealy State Machine
Moore State Machine
Mealy State Machine: Mealy state machine, if outputs depend on both present inputs & present states.
Moore State Machine: Moore state machine, if outputs depend only on present states
Present state variables

## Slide 3: State Diagram
A state diagram or a state transition diagram is a graphical representation among present state, the input, the next state and the output of the finite state sequential machine.
The states are labelled inside the circles & each circle corresponds to one state. Transitions between these states are represented with directed lines. Here, 0 / 0, 1 / 0 & 1 / 1 denotes input / output. - state diagram of Mealy state machine

## Slide 4: State Diagrams
The state diagram of Mealy state machine is shown in the following figure.
The state diagram of Moore state machine is shown in the following figure.
A, B, C & D. States and the respective outputs are labelled inside the circles. Input value is labeled on each transition. there are two transitions from each state based on the value of input, x.
A, B & C States. These states are labelled inside the circles. Transitions between these states are represented with directed lines. Here, 0 / 0, 1 / 0 & 1 / 1 denotes input / output. there are two transitions from each state based on the value of input, x.

## Slide 5: State Table
The state table is a tabular representation of the relationship between the present state, the input, the next state, and the output.
State diagram and state table consists of the same information.

## Slide 6: Transition and Output table
Obtained from state table
Excitationtable:

## Slide 7: Synchronous Sequential Circuit Synchronous sequential circuits are also known as clocked sequential circuits
Moore Machine

## Slide 8: Synchronous Sequential Circuit
Mealy Machine

## Slide 11
State Diagram is known as Mealy Model
D Flip Flop

## Slide 12
Q(t+1) = D(t)
D Flip Flop

## Slide 13
T Flip Flop

## Slide 15
S-R Flip Flop

## Slide 17
J-K Flip Flop

## Slide 19: Serial Binary Adder
Step1: word statement of the problem: the block diagram of a serial binary adder is shown in fig.
it is a synchronous circuit with two input terminals designated X1and X2 which carry the two binary numbers to be added and one output terminal Z which represents the sum.
The inputs and outputs consist of fixed-length sequences 0s and 1s.the output of the serial Zi at time ti is a function of the inputs X1(ti) and X2(ti) at that time ti-1 and of carry which had been generated at ti1.
The carry which represent the past history of the serial adder may be a 0 or 1.
The circuit has two states. If one state indicates that carry from the previous addition is a 0, the other state indicates that the carry from the previous addition is a 1

## Slide 20
Step2 and 3: state diagram and state table: let a designate the state of the serial adder at ti if a carry 0 was generated at ti-1, and let b designate the state of the serial adder at ti if carry 1 was generated at ti-1 .the state of the adder at that time when the present inputs are applied is referred to as the present state(PS) and the state to which the adder goes as a result of the new carry value is referred to as next state(NS). The behavior of serial adder may be described by the state diagram and state table.

## Slide 21
Figures: serial adder state diagram and state table
If the machine is in state A, i.e., carry from the previous addition is a 0, inputs X1=0 and X2=0 gives sum, 0 and carry 0. So the machine remains in state A and outputs a 0.
Inputs X1=1 and X2=0 gives sum, 1 and carry 0, So the machine remains in state A and outputs a 1.
Inputs X1=0 and X2=1 gives sum1 and carry 0. So the machine goes to state A and outputs a 1.
Inputs X1=1 and X2=1 gives sum, 0 and carry 1. So the machine goes to state B and outputs a 0. The state table also gives the same information.

## Slide 22
If the machine is in state B, i.e., carry from the previous addition is a 1, inputs X1=0 and X2=1 gives sum, 0 and carry 1. So the machine remains in state B and outputs a 0. Inputs X1=1 and X2=0 gives sum, 0 and carry 1. So the machine remains in state B and outputs a 0. Inputs X1=1 and X2=1 gives sum, 1 and carry 0. So the machine remains in state B and outputs a 1. Inputs X1=0 and X2=0 gives sum, 1 and carry 0. So the machine goes to state A and outputs a 1. The state table also gives the same information.
Step4: state assignment and transition and output table: The states, A=0 and B=1 have already been assigned. So, the transition and output table is as shown.

## Slide 23
Step 5-To write the excitation table, select the memory element . Obtain the minimal expressions for D and Z in terms of y,x1 and x2 by using k map as shown in fig

## Slide 24
State table for Mealy state machine model
State table for Moore state machine model
Since, in Moore state machine model, the output depends only on the present state, the last column has only output. Criterion criteria

## Slide 25: Design the sequential circuit for the state diagram shown in Fig. given using J-K flip-flops
Present state |  |  | Next state |  |  |  |  |  | Output | 
 |  |  | X=0 |  |  | X=1 |  |  | X=0 | X=1
Q2 | Q1 | Q0 | Q2 | Q1 | Q0 | Q2 | Q1 | Q0 | Y | Y
0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1
Step 1: State table for state diagram
Step 2: State reduction:
From the state table; it is observed that all the states are different; there is no possibility to reduce the state table.

## Slide 26: Step 3: Excitation table for the given state diagram using J-K flip-flop
Present state |  |  | Input | Next state |  |  | Output | Input of the flip-flops |  |  |  |  | 
Q2 | Q1 | Q0 | X | Q2 | Q1 | Q0 | Y | J0 | K0 | J1 | K 1 | J2 | K2
0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | X | 1 | X | 1 | X
0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | X | 1 | 1 | X | 0 | X
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | X | X | 0 | 0 | X
1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | X | 0 | X | X | 0
1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | X | X | 1 | X | 0
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | X | 0 | X | 0 | X
0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | X | 1 | 0 | X | 1 | X
0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | X | X | 1 | 0 | X
1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | X | 0 | X | X | 1
1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | X | X | 0 | X | 1

## Slide 27: Step 4: K Maps for Flipflops inputs

## Slide 28: Step 4: K Maps for Flipflops inputs

## Slide 29: Step 5: logic diagram

## Slide 30: Design the circuit to generate the sequence 02547 Step 1: State diagram
Step 2: State table for the State diagram
Present state |  |  | Next state |  | 
Q2 | Q1 | Q0 | Q2 | Q1 | Q0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0
Step 3: State reduction:
From the state table it is observed that all the states are different, there is no possibility to reduce the state table.
Step 4:Excitation table for the state table using J-K flip-flop / Transition Table

## Slide 32: Step 5: Logic diagram

## Slide 33: Lockout condition:
designed to generate the sequence 0-2-5-4-7-0, the states 1, 3 and 6 are the unused states. If by chance the sequence generator to find it self in any one of the unused states, the next state is unknown. It may possible that the sequence generator go from one unused state to another unused states, it never arrive at the used state. The circuit is said to be locked. To avoid the condition of lockout, there is need to design the circuit such that, when the circuit found in unused state the next state should be known and it must be used state. The state diagrams of sequence generate to generate the sequence 0-2-5-4-7-0 with lock out condition as shown

## Slide 34: Analysis Of Clocked Sequential Circuit
Step 1:State table for state diagram
Present state | Next state |  | Output | 
 | X=0 | X=1 | X=0 | X=1
a | c | b | 0 | 0
b | d | c | 0 | 0
c | g | d | 1 | 1
d | e | f | 1 | 0
e | f | a | 0 | 1
f | g | f | 1 | 0
g | f | a | 0 | 1

## Slide 35: The states ‘e’ and ‘g’ are equivalent because the next state and outputs are same for the input X is equal to 0 as well as X is equal to 1; and hence ‘g’ is replaced by ‘e’ and the state ‘g’ is removed from the table.
Step 2: State Reduction
Present state | Next state |  | Output | 
 | X=0 | X=1 | X=0 | X=1
a | c | b | 0 | 0
b | d | c | 0 | 0
c | (g)e | d | 1 | 1
d | e | f | 1 | 0
e | f | a | 0 | 1
f | (g)e | f | 1 | 0
The states ‘d’ and ‘f’ are equivalent because the next state and output are same for the input X is equal to 0 and X is equal to 1;and hence ‘f’ is replaced by ‘d’ and the state ‘f’ is removed from the table
Present state | Next state |  | Output | 
 | X=0 | X=1 | X=0 | X=1
a | c | b | 0 | 0
b | d | c | 0 | 0
c | e | d | 1 | 1
d | e | (f)d | 1 | 0
e | (f)d | a | 0 | 1
The state ‘c’ and ‘d’ are not equivalent because next state is same for input X is equal to 0 and X is equal to 1, but outputs are not same.

## Slide 36
Step 3: State Assignment
Variable Assign value
a 000
b 001
c 010
d 011
e 100
Step 4: Transition/ Excitation Table
Present state | Next state |  | Output | 
 | X=0 | X=1 | X=0 | X=1
Q1Q2Q3 | Q1Q2Q3 | Q1Q2Q3 |  | 
000 | 010 | 001 | 0 | 0
001 | 011 | 010 | 0 | 0
010 | 100 | 011 | 1 | 1
011 | 100 | 011 | 1 | 0
100 | 011 | 000 | 0 | 1
 | Input | Present state | Next State | Inputs to F/F | Output
 |  |  |  |  | X=0
 | x | Q1Q2Q3 | Q1Q2Q3 | D1D2D3 | 
0 | 0 | 000 | 010 | 010 | 0
1 | 0 | 001 | 011 | 011 | 0
2 | 0 | 010 | 100 | 100 | 1
3 | 0 | 011 | 100 | 100 | 1
4 | 0 | 100 | 011 | 011 | 0
8 | 1 | 000 | 001 | 001 | 0
9 | 1 | 001 | 010 | 010 | 0
10 | 1 | 010 | 011 | 011 | 1
11 | 1 | 011 | 011 | 011 | 0
12 | 1 | 100 | 000 | 000 | 1

## Slide 37: Step 5: K Maps

## Slide 38: Example
Design a sequential circuit to recognize the input sequence 1101.
That is, output 1 if the sequence 1101 has been read, output 0 otherwise.

## Slide 39: Assign States
4 states, so we need 2 bits

## Slide 40: State Table

## Slide 41: Input Equations

## Slide 42: Circuit Diagram

## Slide 43: A1 batch(PBL Activity)

## Slide 46: A2 batch: PBL2:
Design a 3-bit gray code Counter